## Slide 1: STA using Prime Time
Date : 01 July 2024

## Slide 2: What’s STA
STA is a method of validating the timing performance of a design by checking all possible paths for timing violations.

## Slide 3: PrimeTime - Overview
• PrimeTime is the Synopsys stand-alone full chip, gate-level static timing analyzer
• Widely-adopted in industry and academia, sign-off tools
• Controlled by Tool command language (TCL) compatible with DC

## Slide 4: PrimeTime - Input/Output
Inputs:
– Netlist file
• Verilog/VHDL/EDIF
– Delay format:
• SPEF/SPF/SDF
– Database file (DB):
• Determine the cell delay
– SDC file:
• Define the design to PT
Outputs: – Timing Analysis Reports

## Slide 5: PrimeTime - STA Flow

## Slide 6: PrimeTime - Setup Design
• Set the search path and the link path
set search_path “lib path”
set link_library “* design.db”
set target_library “design.db”
• Read the design and the libraries
read_verilog top_level.v current_design “top_level“
• Link the top design
link_design

## Slide 7: PrimeTime - Timing Constraint
• Clock Period Constraint (script)
create_clock -period 2 [get_ports clk_in]
# define a clock with a frequency of 500 MHz or 2ns period in PrimeTime
set_clock_uncertainty # [get_clocks clk_in]
# define delay between the clock branches (skew).
For pre-layout
set_propagated_clock [all_clocks]
# specifies that PrimeTime realized the latency for each clock path. This command should be used during post route analysis.
read_sdc top_level.sdc

## Slide 8: PrimeTime - Timing Constraint
• Input Delay – Specify the delay of external logic driving current design
set_input_delay -clock clk_in -max #[get_ports i_*]
• Output Delay – Specify the delay of external logic driven by current design
set_output_delay -clock clk_in -max #[get_ports O_*]
• path delay = cell delay + net delay

## Slide 9: PrimeTime - Path Delay Calculation
– Cell delay is stored in files called Synopsys database files or db files. Database files are read into PrimeTime by the link_path variable
– Net delay is stored in sdf file (post-layout) or calculated by PrimeTime by an internal delay calculator (pre-layout).
set link_library “*.db”
read_parasitics -format SPEF top_level.spef.gz (Required after post lay out)
read_sdf top_level.sdf

## Slide 10: PrimeTime - Working Condition
– Use the worst case delay when testing for setup violations
– Use the best case delay when testing for hold violations
set_operating_conditions
Operating condition is defined in library

## Slide 11: PrimeTime - Timing Exception
• False Path – paths in a design were a designer would not want the timing arcs to be calculated
• Paths not relevant to functional operation of the circuit
• paths which are impossible to exercise
• Paths cross different clock domains
set_false_path –from clk_a –to clk_b
set_false_path –from clk_b –to clk_a

## Slide 12: PrimeTime - Generating Reports
To reduce the size and complexity of the PrimeTime reports, it is recommended to break the design into groups.
Report Timing :
report_timing
Report Violation :
report_constraints
Report Clock Timing :
report_clock_timing
Report QOR :
report_qor

## Slide 13: To start PrimeTime
Working with Prime Time
1. In GUI
pt_shell -gui
2. In Terminal (pt_shell)
working in pt_shell>
3. In terminal using script
working in pt_shell>
instead of using command we use script to run design and report

## Slide 14: Prime Time Lab

## Slide 15: Prime Time Lab

## Slide 16: Prime Time Lab

## Slide 17: Prime Time Lab